## Slide 1: Thermodynamics
Ch 2 : Basic Concepts
2. State properties
Prof. Mohamed Nabil Sabry

## Slide 2: State
The state of a system:
Its nature and characteristics
AT a given instant
State Properties :
Quantitative description of the state
AS IS,
NOT how did the system reach it (the trajectory)
State property  Property of the trajectory
Distance along path (trajectory)
Distance from origin (state)

## Slide 3: Equilibrium
Equilibrium:
Inability to perform a spontaneous
change of state
State properties of a system
CANNOT be defined outside EQUILIBRIUM
Pressure of a system
Uniform Pressure

## Slide 4: Process
Process : continuous transition from state A to state B
A process in “equilibrium”?!!
A process in “quasi- equilibrium”
Cycle :
A set of processes ending by the initial state
d

## Slide 5: State Properties
Extensive Property :
  Proportional to size: Mass, volume, energy, charge, …
Intensive Property :
  Independent of size (same value at each portion):
  Temperature, pressure, electric potential, …
Specific Property :
  Ratio of two Extensive Properties:
  specific volume (=1/Density), specific energy, …
Internal vs external Property : (Temperature vs speed)
60kg
37 C
30kg

## Slide 6: Summary
State & state property
Specific properties
Extensive vs Intensive state properties
Internal vs external state properties
Process; quasi equilibrium; cycle