## Slide 1: Thermodynamics
Ch 2 : Basic Concepts
6. State property: Pressure
Prof. Mohamed Nabil Sabry

## Slide 2: Defining Pressure
DA
Specific (Intensive) Property
Force due to the impact
of molecules on the wall
SI Units: Pa = N / m2 = kg/ms2
Other units
M Pa = 106 Pa;
bar =105 Pa;
atm = 1.013 bar;
psi = 1lb/in2= 6.8948 kPa
torr = 1mmHg=133.32 Pa
After you!
Definition of pressure:

## Slide 3: Measuring Pressure
to measure Patm:
Barometer:
Patm against vacuum
0
Atmospheric
Pressure
P
Absolute
Pressure > 0
Relative Pressure
« gauge » (+ ou -)
P
An example for high P: Bourdon
An example for low P
Manometer
Pabs – Patm = Pgauge= Dr g h
Pabs
Patm
h

## Slide 4: Summary
Pressure is a specific (intensive) property, always > 0
Pressure units Pa, bar, atm, psi, torr
P gauge = P absolute – P atm (can be +ve or -ve)
We can only measure pressure difference