## Slide 1: Thermodynamics
Ch 2 : Basic Concepts
7. State property: Temperature
Prof. Mohamed Nabil Sabry

## Slide 2: What is Temperature?!
Temperature is a measure of the ability:
to transfer calorific energy
Intensive Property
of molecules to transmit their excitation intensity
micro:
macro:
chaotic
Problematic of an objective scale for an intensive property
Extensive property is easy to measure:
1m
Intensive property is difficult:
70C
70C
1kg

## Slide 3: What is a Thermometer?
Example : the volume of a liquid
(mercury thermometer)
Question :
What is the relation:
Thermometric Property (TP)  T?!
Thermometer
Temperature
another
property
effects on
Thermometric Property (TP)

## Slide 4: The “Zero’th” Law!
Thermal
Equilibrium
If
Body A
Body B
And
Body A
Body C
Then
Body B
Body C
Defining equality :
Hence, we can define an arbitrary temperature scale :
Colder
Hotter
For a rational scale :
The thermodynamic temperature scale (see below)
Defining difference :

## Slide 5: Thermometers
h
Mercury
Thermometer
fixed points
T=ah+b
P
h
Ideal Gas
Thermometer ***
Pressure of a gas
at fixed volume
T = aP
Resistance
Thermometer
Resistance of a metal (Platinum)
R
R = a + bT + cT2
G
Thermocouple
T1
T2
V = S (T2-T1)
Metal A
Metal B
V

## Slide 6: Importance of assumption!
-
-25
1.0002
0
1.0029
25
1.0121
50
1.0259
75
1.0435
100
Gas
Thermo-
meter
Water Therm.
Alcohol Therm.
Mercury Therm.
t
v
-
0
6.2
27.5
59.4
100
t*
1.2167
1.2475
1.2800
1.3170
1.3604
1.4116
-18.8
0
19.8
42.4
68.8
100
v
t*
0.073220
0.073556
0.073890
0.074225
0.074561
0.074898
-25.0
0
24.9
49.9
74.9
100
v
t*
v specific volume (cm3/g)
t* Temperature assuming linear in v (C)

## Slide 7: Summary
Temperature T is an intensive property that measures the ability to transfer heat
Thermometers require:
  An assumption relating TP with T
  A set of fixed points to calibrate it
The Zeroth Law defines equality of temperature
It is measured indirectly through its effect on another (measurable) thermometric property (TP) : thermometer
The ideal gas thermometer is the most accurate