## Slide 1: Thermodynamics
Ch3 : Energy Concepts & First Law
4. Internal energy and heat
Prof. Mohamed Nabil Sabry

## Slide 2: Internal Energy (qualitative)
Suppose we have N molecules each of mass m
Mass of body M = m * N
is the absolute velocity of molecule i
Body velocity
= average velocity
We can define:
Deviation,
vibration
Kinetic Energy of N molecules:
By substituting
KE of body
KE of molecules
= 0
(average of deviations)
=

## Slide 3: Internal Energy : Generalization
Internal Energy U = (SKE + SPE + S Chemical + S Nuclear + ..) of molecules
Stored Energy
Similarly:
In general:
Kinetic Energies KE
KE of the body
KE of random molecules speed
=
+
Potential Energy PE
PE of the body
=
+
u = U/m = Specific Internal Energy
Internal Energy
PE of intermolecular forces

## Slide 4: Heat
A power that crosses the boundary
Due to a temperature difference
NOT associated with a transfer of matter
Heat power is:
+ve
-ve
Sign Convention
Heat transferred is path dependent
Heat
Work
U + Flow Work
DU
System: Water in a tea pot.
What are energies involved?
Distinguish between heat (energy that crosses)
and internal energy (energy stored in a hot body)
!
!
!
No heat!
(associated
with a flow)
Heat Power in Watt
Heat : Q in Joule
Enthalpy H

## Slide 5: Summary
Internal energy is an energy that is
associated with molecules. It combines:
Kinetic energy of Brownian motion
Potential energy of intermolecular forces
Chemical and nuclear energies
Heat power is defined as:
A power that crosses the boundary
Due to a temperature difference
NOT associated with a transfer of matter
Internal energy + Flow work  Enthalpy