## Slide 1: Thermodynamics
Ch4 : Pure Substance & Eqs. of state
3. Ideal Gases
Prof. Mohamed Nabil Sabry

## Slide 2: State Equations
Assume a number F (degrees of Freedom) of state variables are given:
All other state variables can be expressed in terms of them
These relations are:
State Equations
Thermal equation of state :
Calorific equations of state
(v = 1/r)
Mainly 2 kinds:
f ( P, T, v) = 0
u = f1 ( P, T)
h = f2 ( P, T)

## Slide 3: Perfect (Ideal) Gas
Hypotheses:
Low density
  volume of molecules Negligible
  intermolecular forces Negligible
  time of impact Negligible
Molecular collisions are perfectly elastic
(No energy loss during impact)
x
y
z
L
Plan W
of area A
Change of the momentum of a particle
during collision with the plan W (component in y):
D (momentum) = m0 (vy – (– vy) = 2m0vy
Average Time between 2 collisions on the plan W:
Dt = 2 L / vy
Pressure due to a molecule:
P1 molecule = Force/A =
[D (momentum)/Dt ]/A = m0vy2 / V
P V = m0 S vy2
For N molecules:
Plan W'

## Slide 4: Equation of State for a perfect gas
P v = R T
_
_
P v = R T
P V = n R T
_
P V = m R T
Gas Constant: R = R / m
(m molecular mass)
_
Principle of equipartition of energy:
S vy2= S vx2= S vz2= 1/3 S v2= 1/3 N vrms2
perfect gas  T  average kinetic energy of a molecule
k T = 1/3 m0 vrms2
Boltzmann
Universal Gas Constant
P V = N k T = n NA k T = n R T
moles
Avogadro
R = NAk = 8314.5 J/kmol K
_
_
P V = m0 1/3 N vrms2
n = m / m
(m mass of gas)
P V = m0 S vy2

## Slide 5: Summary
Hypotheses for an ideal gas:
  Low density  negligible:
    Molecules volume
    Intermolecular forces
    Time of collision
  Elastic collisions
Equipartition of kinetic energy by direction
Ideal Gas thermal equation of state: P v = R T
Gas constant R = R / m
Universal gas constant R = NA kB = 8314.5 J/kmol K
_
_
kB T = 1/3 m0 vrms2