## Slide 1: Thermodynamics
Ch4 : Pure Substance & Eqs. of state
5. Calorific Eqs. Of State

## Slide 2: Energy Properties
J
J/kg
J/kmol
Total
Internal
Energy
E
e
e
Energy
U
u
u
Enthalpy
H
h
h
Thermal Capacities
(Specific heats)
Thermal Capacities at constant volume
cv = u /  T |v
cP =  h /  T |P
Thermal Capacities at constant pressure
Ratio of thermal capacities: g = cP / cv
(Specific heats ratio)
Internal
cv =  u /  T |v= m cv
cP =  h /  T |P = m cP

## Slide 3: Calorific Eq. of State – Perfect Gas
k T = 1/3 m0 vrms2
Reminder:
Assuming translational movement only (degrees of freedom f = 3)
+ principle of equipartition of energy:
f k T/2 = 1/2 m0 vrms2 = KE for one molecule
No. of molecules in 1 kg: NA / m
u = (NA k/m) (f/2)T = R (f /2) T
h = u + Pv = R (1 + f /2) T
cv =  u/ T|v=const = R (f /2)
cP =  h/ T|P=const = R (1+f /2)
In general, if f  3:
For a perfect gas, u is composed of KE only (no intermolecular forces)
Also:
g = cP/cv = (f+2) / f
cP - cv = R
Du = cv DT; cv = R / (g – 1)
Dh = cP DT; cP = g R / (g – 1)

## Slide 4: Variation of Internal Energy with temperature (qualitative)
+ Dissociation
+ Ionization + ...
PE
Liquid
gas
Temperature increases
KE
translation
+rotation
+vibration

## Slide 5: Gas, large variations of temperature 1
Mono atomic
(Argon, Neon, …)
Diatomic
(O2, N2, …)
Poly atomic
(CO2, NH3, …)
Translation f = 3 f = 3 f = 3
To estimate thermal capacities of a perfect gas:
f  g = (f+2) / f  cv = R/(g-1)  cP= g cv
To
estimate f:
+Rotation +0 +2 +3
+Vibration +0 +1 +n?
But f depends on temperature T and the nature of molecules
Temperature
Low
Medium
High
Movement

## Slide 6: Gas, large variations of temperature 2
If
Gas
Very small density
Large variation of T
Then:
Pv = RT
cP, cv = f(T)
u, h = f(T)
are
not f (P)
cv =  u/ T| v = du / dT
cP =  h/ T|P = dh / dT = d(u+Pv)/dT = d(u+RT)/dT = cv + R
cP = f (T) at low pressure is given in tables, hence:
cv
T
Every degree of freedom
is activated at a given
temperature.
Translational Energy
+ Rotational Energy
+ Vibration Energy
Typical variation of cv
At low pressure:
~Tamb
Semi-ideal
gas
h =  cP dT; cv = cP – R; u =  cv dT

## Slide 7: Calorific Eq. of state – Other phases
u = x ug + (1-x) uf
h = x hg + (1-x) hf
Latent heat :
hfg = hg - hf
cP  
For a mixture
liquid-vapor:
For a solid or liquid:
cP = cv = c
For crystals
at ambient temperature:
c = 3 R / m
_

## Slide 8: Summary
Definition of cv, cp, g and f
Gas Thermal Calorific Thermal
Model State eq. State eq. capacities
Ideal P v = R T u, h  T cv ,cP = const,
(Small DT) cP - cv = R;
cv=R/(g-1); cp=gR/(g-1)
g = (f + 2) / f
Semi-Ideal P v = R T u, h = f(T) cv ,cP = f(T),
(ideal +Large DT) cP - cv = R
Real P v ≠ R T u, h = f(T,P) cv ,cP = f(T,P)
Effect of temperature variations
on heat capacities