## Slide 1: Thermodynamics
Ch4 : Pure Substance & Eqs. of state
5. Real Gases

## Slide 2: Van Der Waals Equation of state
Volume of molecules non negligeable
Intermolecular forces non negligeable
Van der Waals (VDW):
Postulated forme
(P + a/v2) (v - b) = R T
(a,b const.)
Putting: at the critical point (P=Pc ; T=Tc):
P/v|T= 2P/v2|T=0
(PR + 3/vr'2) (3vr' - 1) = 8 TR
where PR=P/Pc; TR=T/Tc;
vr'=v/vc' ; vc'=3RTc/8Pc
L
L+G
P
v
T=T3
G
T=Tc
c
!
The precision of VDW is better than Pv=RT; BUT not perfect
It all depends on reduced properties

## Slide 3: Compressibility – Law of Corresponding States
Compressibility: Z = Pv / RT
Law of corresponding states :
Definition
For all Gases : Z = f (PR, TR)
where PR = P / Pc ; TR = T / Tc
For a perfect gas Z = 1
N.B. 1: If gas at low density
(ex. PR <0.1 and/or TR >5) then Z1
N.B. 2: The law of corresponding states is approximate (error <2.5%)
Z
PR
1
1
TR=0.8
TR=1.2
TR=5.0
vR = v Pc / RTc
To correct the error: use the ‘Acentric factor’ (eccentricity) – see tables

## Slide 4: Compressibility – Enthalpy departure
Law of corresponding states
also applies:
TR
PR
h is the required molal specific enthalpy
h* is the molal specific enthalpy
At a very small pressure (semi-ideal)
_
_

## Slide 5: Summary
Hypotheses for Van Der Waals eq.:
Law of corresponding States
Compressibility Z = P v / R T
Compressibility charts:
  Correction of thermal eq. of state
  Correction of calorific eq. of state
Volume of molecules non negligeable
Intermolecular forces non negligeable
(PR + 3/vr'2) (3vr' - 1) = 8 TR
where PR=P/Pc; TR=T/Tc;
vr'=v/vc' ; vc'=3RTc/8Pc