## Slide 1
Ch5 : Applications of First Law
2. Open System Processes – B
Thermodynamics

## Slide 2: SSSF: Case II: Heat exchangers: Q ≠ 0; W = 0
Usually, we neglect:
Pumping and/or mixing work,
KE & PE,
Heat lost to surroundings
Compared to heat exchanged
mA hAin
mA hAout
mB hBout
mB hBin
System C
System A
System B
Q
System A:
QA = mA (hAout - hAin)
System B:
QB = mB (hBout - hBin)
System C:
mA (hAout - hAin) = - mB (hBout - hBin)
QA = - QB

## Slide 3: SSSF: Case III: Fluid machines: W  0
Work > 0
Work < 0
Liquid
Gas
Pump
Fan
Compressor
Usually we neglect:
Heat
KE + PE
wrt work
q - w = h2 - h1
- w = h2 - h1 + D KE
Blower
Turbine
Fluid
entering
at high
pressure
Fluid
leaving
at low
pressure
Classification according to DP
P2  P1
P2 > P1
P2 >> P1
W / m = w = h1 – h2
.
.
Except for:
Cooled Compressor
KE for a fan

## Slide 4: Non-Steady Flow: Filling a tank
High pressure line
High pressure line
Before filling
After filling
Rigid tank
Valve
Iff rigid tank: V is const., W = 0
Energy balance: Q – 0 + min(hline + ½ v2) – 0 = (m u)|after – (m u)|before
Mass balance: min= mafter – mbefore
Rigid tank: (m v)|after = V = (m v)|before
+ model: thermal eq. of state + calorific eq. of state
 Solve the problem!

## Slide 5: Summary
Unsteady flow: Filling tank
For an open system – B
Heat exchangers Q ≠ 0; W = 0
.
.
Usually neglect KE, PE, Q to ambient
Fluid Machines W ≠ 0
.
Usually neglect KE, PE, Q:
Turbine, pump, fan (KE), blower, compressor (Q)
Entering mass carries h, KE
Both stored mass and u increase
d/dt (.) ≠ 0
min ≠ 0; mout = 0
Steady flow: Continued