## Slide 1: Thermodynamics
Ch6 : Second Law
2. Heat Engines

## Slide 2: Definitions
A Heat reservoir is a body of high thermal capacity, allowing it to
exchange heat
without changing its temperature
T = Const
Q
A Heat engine is a device working on a
Cycle to exchange Heat  Work

## Slide 3: 1- Motor
Evaporator
Condenser
Heat Reservoir
at Tc (Cold)
Heat Reservoir
at Th (Hot)
Qh
Qc
Pump
Wp
Turbine
Wt
|Work| = |V dP |
(Vgas >> V liq)
|Wt| >> |Wp|
W = |Wt| - |Wp| > 0
Qc cannot be reused in the cycle
(Tc < Th)
Qh has not been entirely transformed into work
We define Efficiency:
h = |W| / |Qh| < 1
Liquid
vapor
High P
Low P
Steam Power Plant
Qh
Qc
W
|Qh| - |Qc| = W
(1st Law)

## Slide 4: 2- Refrigerator, Heat Pump
Qh
Qc
Compressor
W
Throttling
Coefficient of performance COP
Refrigerator
COPrefrig = |Qc| / |W|
Heat Pump
COPhp = |Qh| / |W| > 1
NB: |Qh| = |W| + |Qc|
High P
Low P
liquid
vapor
Condenser
Evaporator
Heat Reservoir
at Th (Hot)
Heat Reservoir
at Tc (Cold)
Qh
Qc
W

## Slide 5: Summary
Heat engine: A cycle to exchange Work  Heat
Refrigerator: COPref = |Qc| / |W|
Heat Engines
Types of heat engines by purpose
Motor: Efficiency h = |W| / |Qh| < 1
Heat pump: COPhp = |Qh| / |W| > 1