## Slide 1: Thermodynamics
Ch6 : Second Law
4. Carnot Cycle and Principles

## Slide 2: Carnot Cycle
Process 1-2 Isothermal
  T = Th
  |Heat added| = Qh
P
V
1
2
3
4
Qh
Qc
T = Th
T = Tc
adiabatic
adiabatic
Net Work |W | = |Qh | - | Qc |
Reversible Cycle
Process 2-3 Adiabatic
  Heat = 0
Process 3-4 Isothermal
  T = Tc
  |Heat rejected| = Qc
Process 4-1 Adiabatic
  Heat = 0

## Slide 3: Carnot Cycle for a perfect gas
For a perfect gas:
PV = m R T; dU = mcv dT
Process 1 - 2:
|Qh| = |W12| = mR Th ln (V2/V1)
Process 3 - 4:
|Qc| = |W34| = mR Tc ln (V3/V4)
h = 1 – (Tc /Th ) [ln (V3/V4) / ln (V2/V1)]
For adiabatic processes:
V3 / V4 = V2 / V1
h = 1 - Tc /Th
P
V
1
2
3
4
Qh
Qc
T = Th
T = Tc
adiabatic
adiabatic
T2 / T3 = (V3 / V2)(g-1) =T1 / T4 = (V4 / V1)(g-1)
|Qc| / |Qh| = Tc / Th
|Qc| / Tc = |Qh| / Th
h = (|Qh| – |Qc|) /|Qh| = 1 – |Qc| /|Qh|

## Slide 4: Carnot Principles - 1
It is impossible to construct a motor operting between 2 reservoirs
having an efficiency that is better than a reversible motor
operating between the same reservoirs
1 - "Carnot" is the best!
Qc'
Tc
Th
Another
Motor claiming
a better h
than Carnot !
A reversible
motor
{ex: Carnot}
Qc
Qh'
W
Qh
Suppose h' > h :
{
Let us invert the
reversible motor
{ex: Carnot}:
Heat Pump
By joining the 2 machines:
|W/Qh'| > |W/Qh|
|Qh' | < |Qh |
|Qc' | < |Qc |
|Qc | - |Qc' |
|Qc | - |Qc' |
|Qc | - |Qc' | goes from cold to hot
Spontaneously: Impossible!

## Slide 5: Carnot Principles - 2
All other "Carnots" are as good !
All reversible motors working between the
same heat reservoirs have the same efficiency
Proof:
Put them in parallel,
Reverse one of them
Use the preceding principle
The efficiency of a reversible motor,
working between 2 heat reservoirs
depends only on Th andTc
(i.e. not function of the nature matter nor the cycle used)
h reversible = f( Tc , Th )  system matter
Base for a thermodynamic temperature scale
Th
Qc
W
Qh
Tc
Qc'
W
Qh'

## Slide 6: Performance of heat engines
By definition, whether the machine was reversible or not:
COPref=Qc/W=Qc/(Qh-Qc)
For a motor
For a refrigerator
For a heat pump
For a reversible machine, Qh/Th=Qc/Tc, hence:
COPhp=Qh/W=Qh/(Qh-Qc) >1
h=W/Qh=1- Qc/Qh < 1
COPref reversible=Tc/(Th-Tc)
COPhp reversible=Th/(Th-Tc) >1
h reversible=1- Tc/Th < 1
Absolute value of heat exchanged with the hot reservoir: Qh
Absolute value of heat exchanged with the cold reservoir: Qc
Absolute value of work: W = Qh - Qc
The performance of a reversible machine is always the best possible
hreversible  hirrev
COPref reversible  COPref irrev
COPhp reversible  COPhp irrev
Notation:

## Slide 7: Summary
Carnot cycle: Reversible 4-processes (2 isotherm+2 adiabatic)
Reversible performance 
Irreversible performance (all Engines)
Carnot cycle and principles
Efficiency h = 1 – Tc / Th
Motor: h = (|Qh| – |Qc|) / |Qh| if reversible: = 1 – Tc/Th < 1
All reversible heat engines:
Same performance
|Qh| / Th = |Qc| / Tc
Carnot Principles
Coefficients of performance
Always: |W| = |Qh| – |Qc|
Refrigerator: COP = |Qc| / (|Qh| – |Qc|) if reversible: = Tc / (Th – Tc)
Heat pump : COP = |Qh| / (|Qh| – |Qc|) if reversible: = Th / (Th – Tc) > 1