## Slide 1: Thermodynamics
Ch6 : Second Law
5. Thermodynamic Temperature Scale

## Slide 2: Thermodynamic temperature scale T'
hreversible = 1- f(Tc' ,Th')
What is the form of f(Tc',Th') ?
Tm'
A
B
C
Compare between motors A,B on one side
and C (all are reversible hence same global efficiency)
Qh
Qh
Qc
Q'c
Qm
WC
WA
WB
Qm
hC = WC / Qh = 1 - QC/Qh = 1- f(Tc' ,Th')
WC = WA+WB
QC = Q'C
hA = WA / Qh = 1 - Qm/Qh = 1- f(Tm' ,Th')
hB = WB / Qm = 1 - QC/Qm = 1- f(Tc' ,Tm')
1
2
3
For the same Qh
hreversible depends only on temperatures Th', Tc'
Possibility to define a thermometer: measure h , get T'
Th'
Tc'

## Slide 3: Equivalence with perfect gas temperature
f(Tc' ,Th') = f(Tc' ,Tm') * f(Tm' ,Th') Tm'
hC : QC/Qh = f(Tc' ,Th')
hA : Qm/Qh = f(Tm' ,Th')
hB : QC/Qm = f(Tc' ,Tm')
1'
2'
3'
x
f(Tc' ,Th') = g(Tc') / g(Th')
T' = T
Perfect gas Temperature = Thermodynamic temperature scale
Pose g(T') = T'
h reversible = 1 - Tc' / Th'=hCarnot – Perfect Gas=1-Tc/Th
h = 1- g(Tc') / g(Th')

## Slide 4: Summary
There is an OBJECTIVE temperature scale
Thermodynamic temperature scale
Based on Carnot principles
Thermodynamic Temperature Scale
To measure the:
Use:
Ideal Gas Thermometer