## Slide 1: Thermodynamics
Ch7 : Entropy
Examples

## Slide 2: Example 7.1
  A heat reservoir at 227oC loses 600J of heat to an ambient air at 27oC. Assuming process within the reservoir is reversible (uniform T), find the entropy change of the reservoir, of air and of the whole universe.
227 oC
27 oC
  600 J
System: 3 systems: 1) The heat reservoir; 2) Ambient air; 3) Universe (sum of all systems)
Conservation: Only energy
Energies: Heat.
Process: Heat transfer
Properties: Reservoir and air temperatures
Model: Quantitative expression of the Second Law
Extensive: yes, 1 value: Heat
Common model to all systems: DS = S Qi/Ti + DSirrev
System 1: Heat reservoir:
Within the reservoir DSirrev = 0 (internally reversible).
DSreservoir = – 600 / (227+273) = – 1.2 J/K
(heat is rejected)
System 2: Air:
Within air DSirrev = 0 (internally reversible).
DSair = +600 / ( 27+273) = +2.0 J/K (heat is added)
System 3: Universe = Reservoir + Air:
Total heat = 0
(no heat crossing universe boundaries).
DSuniverse = DSreservoir + DSair = 2 – 1.2 = 0.8 J/K > 0 (irreversible process)

## Slide 3: Example 7.2 a
A cycle is performed on 1 kg of air as shown in figure. Process 12: Reversible isobaric heating from 11 bar and 60 ºC to 280 ºC; Process 23: Irreversible adiabatic expansion to 0.7 bar and 4.5 ºC; Process 34: Reversible isothermal cooling; Process 41: Isentropic compression. Calculate the entropy change, the internal entropy production and Ʃi qi /Ti for each process as well as for the cycle, assuming that air behaves as: a) Ideal gas; b) Semi-ideal gas. Find also the efficiency of the cycle 1234 and that of the reversible cycle 123'4, and compare both to the Carnot's efficiency between the same maximum and minimum temperature
T
s
1
2
3
3'
4
Answer:
System: Air (closed system)
Conservation: Only energy
Energies: Heat, Work and Internal energy.
Process: A cycle composed of 4 given processes
Properties: State 1: P1, T1 given  complete;
State 2: T2 given, process 1-2 isobaric: P2 = P1  complete;
State 3: P3, T3 given  complete;
State 4: process 3-4 is isothermal T3 = T4, Process 4-1 is isentropic s3 = s4  complete
Model: Second Law + ideal gas or semi-ideal gas for air
Extensive: yes, 1 value: mass m = 1kg
11 bar
60oC
280oC
4.5oC
0.7 bar

## Slide 4: Example 7.2 b
In general:
We need to use both forms of the second law:
Δs = Ʃi qi /Ti + Δsirrev = ʃ (dh – vdp)/T
cp = 1.005 kJ/kg.K, Δs = cp ln T2/T1 – R ln P2/P1
Δs = so(T2)– so(T1)– R ln P2/P1 so values are obtained from air tables as a function of T
Process 2-3: Irreversible adiabatic Ʃi qi /Ti = 0
Δs = Δsirrev
s3 – s2 = cp ln T3/T2 – R ln P3/P2
= 1.005 * ln (277.5/553) – (8.3143/28.97)* ln (0.7/11)
= 0.0975 kJ/kg.K = Δsirrev
s3 – s2 = so(T3) – so(T2) – R ln P3/P2
= 1.624 – 2.324 – (8.3143/28.97)* ln (0.7/11)
= 0.0905 kJ/kg.K = Δsirrev
Process 1-2: Reversible isobaric Δsirrev = 0
s2 – s1 = Ʃi qi /Ti
s2 – s1 = cp ln T2/T1 = 1.005 ln (553/333)
= 0.5098 kJ/kg.K = Ʃi qi /Ti
s2 – s1 = so(T2) – so(T1) = 2.324 – 1.807 = 0.517 kJ/kg.K
= Ʃi qi /Ti (from air tables at T2, T1)
Process 3-4: Reversible isothermal Δsirrev = 0
Δs = Ʃi qi /Ti
But, s4 = s1  s4 – s3 = - ((s3 – s2) + (s2 – s1))
s4 – s3 = - 0.0975 – 0.5098 = – 0.6073 kJ/kg.K = Ʃi qi /Ti
s4 – s3 = – 0.0905 – 0.517 = – 0.6075 kJ/kg.K = Ʃi qi /Ti
Process 4-1: Isentropic compression Δs = Ʃi qi /Ti = Δsirrev =0
T
s
1
2
3
3'
4
11 bar
60oC
280oC
4.5oC
0.7 bar

## Slide 5: Example 7.2 c
For the cycle 1234: Δs = 0 because it is a cycle
Ʃi qi /Ti = 0.5098 + 0 – 0.6073 + 0 = – 0.0975 kJ/kg.K
N.B.: Above quantity is negative because cycle is irreversible – Clausius inequality
Δsirrev = 0 + 0.0975 + 0+ 0 = 0.0975 kJ/kg.K
N.B.: Above quantity is positive because irreversible
qh = q12 = h2 – h1 = 1.005 * (553 – 333) = 221.1 kJ/kg
|qc| = |q34| = T |s4 – s3| (reversible isothermal)
= 277.5 * 0.6073 = 168.5 kJ/kg
hirrev = 1 – (qc/qh) = 1 – (168.7/221.1) = 23.8 %
Ʃi qi /Ti = 0.517 + 0 - 0.6075 + 0 = – 0.0905 kJ/kg.K
Δsirrev = 0 + 0.0905 + 0+ 0 = 0.0905 kJ/kg.K
qh = q12 = h2 – h1 = 557.9 – 333.4 = 224.5 kJ/kg.K
|qc| = |q34| = T (s3 – s4) = 277.5 * 0.6075 = 168.6 kJ/kg
hirrev = 1 – (qc/qh) = 1 – (168.6/224.5) = 24.9 %
N.B. Cycle efficiency is lower than Carnot, because heat is added at an average temperature that is lower than the highest temperature based on which Carnot efficiency has been calculated.
For the cycle 123’4:
qh = q12 = h2 – h1 as before
|qc| = |q34| = T4 (s2 – s1)
since s3' = s2, s4 = s1
qh = 221.1 kJ/kg.K
|qc| = 277.5 * 0.5098 = 141.5 kJ/kg
hrev = 1 – (qc/qh) = 1 – (141.5/221.1) = 36 %
N.B. reversible efficiency is greater than irreversible cycle efficiency – Carnot principle
qh = 224.5 kJ/kg.K
qc = 277.5 * 0.517 = 143.5 kJ/kg
hrev = 1 – (qc/qh) = 1 – (143.5/224.5) = 36.1 %
Carnot cycle efficiency between
Th = 553 K, Tc= 277.5 K is
hcarnot = 1 – (Tc/Th) = 1- (277.5/553) = 49.8 %
T
s
1
2
3
3'
4
11 bar
60oC
280oC
4.5oC
0.7 bar

## Slide 6: Example 7.3 a
Air at 1 bar and 24 ºC is adiabatically compressed in a steady flow process to 1.7bar with an isentropic efficiency of 85%. The inlet and outlet velocities are 10 and 40 m/s respectively. Determine the final temperature, work and entropy change assuming that air behaves as: a) Ideal gas b) Semi-ideal gas.
T
s
1
2'
2
P1
P2
System: Air in compressor (open steady flow)
Conservation: Only energy
Energies: Work, Enthalpy and Kinetic energy; No Heat.
Process: Compression with an isentropic efficiency
Properties: Point 1: P1, T1 given = complete; Point 2: P2 given; other property from process
Model: a) Ideal gas; b) Semi-ideal gas
Extensive: None
First, we have to calculate the isentropic process between the same pressures
To get the final temperature
Process 12': we now consider the reversible adiabatic process 12':
Isentropic + Ideal : either use Ds=0=cpln(T2/T1)-Rln(P2/P1) or use Pvγ = c
But for air γ = 1.4 then
T2' = T1 (P2/P1) (γ-1)/γ
= 297 * (1.7/1) (0.4/1.4) = 345.62 K
Isentropic + Semi-ideal
P2’/P1 = Pr2’/Pr1 (From tables at 297 K, Pr1 = 1.34)
Pr2' = 1.34*(1.71/1) = 2.278
From gas tables at the obtained Pr get T2' = 345.61 K

## Slide 7: Example 7.3 b
Process 12: we now consider the adiabatic irreversible process 12:
his = (h2'-h1)/ (h2-h1)
For ideal gas h = cpT then:
0.85 = (345.62-297)/ (T2-297)  T2 = 354.2 K
b) Using gas tables to relate h and T then:
0.85 = (346.07–297.2)/ (h2–297.2) h2 = 354.7 kJ/kg, T2 = 354.2 K
T
s
1
2'
2
P1
P2
To get the work, from the first law we have:
q12 – w12 = (h2 – h1) + (v22 – v12)/2 q12 = 0
then:
For ideal gas h = cpT
-w12 = 1.005(354.2 – 297) + (402 – 102)/2000 w12 = -58.24 kJ/kg
b) Using gas tables
-w12 = (354.7 – 297.2) + (402 – 102)/2000  w12 = -58.25 kJ/kg
To get the entropy change
s2 – s1 = cp ln T2/T1 – R ln P2/P1
= 1.005 ln (354.2/297) – (8.3143/28.97) ln (1.7) = 0.0247 kJ/kg.K
b) s2 – s1 = s0(T2) – s0(T1) – R ln P2/P1
= (1.8698 – 1.6885) – (8.3143/28.97) ln (1.7) = 0.029 kJ/kg.K

## Slide 8: Example 7.4 a
Steam expands in a turbine from 30 bar, 500 ºC to 0.2bar adiabatically. If the steam flow rate is 2 kg/s, what is the maximum power that could be obtained from this turbine? What is the power and the final state of the steam when the isentropic efficiency is 90%
Answer:
System: Steam in turbine (open steady flow)
Conservation: Only energy
Energies: Work, Enthalpy; No Heat.
Process: Expansion with an isentropic efficiency
Properties: Point 1: P1, T1 given  complete;
Point 2: P2 given; other property from process
Model: Steam tables
Extensive: Yes 1: mass flow rate ṁ
T
s
1
2'
2
P2
P1
30 bar, 500oC
2 kg/s
0.2 bar
adiabatic
his=90%

## Slide 9: Example 7.4 b
The 1st law for steady flow without KE, PE is
q12 – w12 = (h2 – h1) but for adiabatic process q12 = 0  – w12 = (h2 – h1)
Maximum work (and hence power) is for reversible process.
Process 12' is reversible adiabatic
From steam chart at 30 bar, 500 ºC: h= 3456.5 kJ/kg s= 7.234 kJ/kg.K
From steam chart at 0.2 bar, s= 7.234:
sf = 0.8319 kJ/kgK sg = 7.9085 kJ/kgK sf<s<sg hence wet steam
x2' = (s-sf)/(sg-sf) = 0.9047
hf = 251.38 kJ/kg hg = 2609.7 kJ/kg
h2' = x hg + (1-x) hf = 2384.9 kJ/kg
Maximum power = ṁ (h2’ – h1) = 2*(3456.5 – 2384.9) = 2143.2 kW
The actual (irreversible) adiabatic process is 13
his = (h2-h1)/ (h2’ – h1) = 90%
h2 = 3456.5 – 0.9*(3456.5- 2384.9) = 2492 kJ/kg
Power = his Pmax = ṁ (h3 – h1) = 0.9*2143.2 = 1928.8 kW
Final state at 0.2 bar, h2= 2492 < hg wet steam  t= 60.1ºC,
x2= (h2-hf)/(hg-hf) = 0.95
s2=x2 sg + (1-x2) sf = 7.555 kJ/kgK
T
s
1
2'
2
P2
P1

## Slide 10: Example 7.5 a
Steam is compressed isothermally in a reversible steady flow process from 1.2bar and 250ºC to 10bar. Find the change of entropy, the heat and work exchanged in this process assuming that the steam is a) Real gas b) Ideal gas c) Semi-ideal gas
Answer:
System: Steam in compressor (open steady flow)
Conservation: Only energy
Energies: Work, Heat and Enthalpy.
Process: Isothermal compression
Properties: Point 1: P1, T1 given  complete;
Point 2: P2 given, T2 = T1  complete
Model: 3 models: a) Steam tables; b) Ideal gas; b) Semi-ideal gas
Extensive: None
1.2 bar,
250oC
10 bar
Isothermal

## Slide 11: Example 7.5 b
Since the process is reversible  Δsirrev = 0
And since T is constant  s2 – s1 = q12 /T
At 1.2 bar and 250 ºC: s1 = 7.957 kJ/kg.K h1 = 2974.2 kJ/kg
At 10 bar and 250 ºC: s2 = 6.923 kJ/kg.K h2 = 2942 kJ/kg
s2 – s1 = 6.923 – 7.957 = –1.034 kJ/kg.K
q12 = T (s2 – s1) = (250+273)*(-1.031) = – 540.78 kJ/kg
From the 1st law for steady flow
w12 = q12 – (h2 – h1) = - 540.78 – (2942 – 2974.2) = –508.8 kJ/kg
b) If the steam is assumed to be ideal gas:
s2 – s1 = cp ln T2/T1 – R ln P2/P1
= - (8.3143/18) ln (10/1.2) = - 0.979 kJ/kg.K
q12 = T (s2 – s1) = (250+273)*(- 0.979) = - 512 kJ/kg
The work could be obtained either from the 1st law:
w12 = q12 – cp (T2 – T1) = q12 = – 512 kJ/kg
Or from: w12 = ʃPdv = RT ʃdv/v = RT ln (v2/v1)
= - RT ln (P2/P1) = - (8.3143/18)*523 ln (10/1.2) = – 512 kJ/kg
The only difference between ideal and semi-ideal gas is that cp depends on T. when T is constant both cases give the same results!
The only difference would be in the average value of cP used; which was irrelevant in this example

## Slide 12: Example 7.6 a
A membrane separates an insulated rigid vessel into 2 rooms A and B. Room A contains 2 kg of CO at 120ºC and 3bar. Room B contains 3 kg of O2 at 5bar and 75 ºC. if the membrane ruptures, and the two gases mix, find the final temperature and pressure, the partial pressure of each gas in the mixture and the change in entropy
Answer:
System: 3 systems: A) CO in room A; B) O2 in room B; mix) Mixture; all are closed
Conservation: Mass and Energy
Energies: Internal energies; No Work, No Heat.
Process: Mixing in a confined space (Volume of each system is fixed)
Properties: System A: PA, TA given  complete;
System B: PB, TB given  complete;
System 3: all properties are to be calculated from process
Model: ideal gas mixtures
Extensive: Yes 2: masses of A and B  deduce mass of mix
System A:
Initial volume of A: VA = mA RA TA / PA = 2*(8314.5/28)*(120+273)/(3*105) = 0.778 m3
Initial internal energy: cvA = RA/(gA-1) = (8314.5/28)/(1.4 – 1)/1,000 = 0.742366 kJ/kg K
 UA = mA cvA TA = 2*0.742366*(120+273) = 583.5 kJ
2 kg CO
120oC
3 bar
3 kg O2
75oC
5 bar
System B:
Initial volume of B: VB = mB RB TB / PB = 3*(8314.5/32)*(75+273)/(5*105) = 0.543 m3
Initial internal energy: cvB = RB/(gB-1) = (8314.5/32)/(1.4 – 1)/1,000 = 0.64957 kJ/kg K
 UB = mB cvB TB = 3*0.64957*(75+273) = 678.15 kJ

## Slide 13: Example 7.6 b
System mix:
The conservation of mass gives:
m mix = mA + mB = 2 + 3 = 5 kg
And hence the mass fraction of each gas is
xCO = 2/5 = 0.4 xO2 = 3/5 = 0.6
From which we can get the mixture molecular weight
mT = 1 / (i xi / mi) = 1/ ((0.4/28) + (0.6/32)) = 30.27
And hence the mole fraction can be calculated
yCO = mT fCO / mCO = 30.27 * (0.4/28) = 0.432
yO2 = mT fO2 / mO2 = 30.27 * (0.6/32) = 0.568
The volume of the mixture is equal to the sum of the volumes of the two rooms:
Vmix = VA + VB
From which we can easily calculate Pmix = m mix Rmix Tmix / Vmix
 Pmix = 3.82 bar
The conservation of energy gives:
Q – W = ΔU + ΔKE + ΔPE
Uafter = Ubefore  Umix= UA + UB
Umix = mmix cv mix Tmix (assume ideal gas)
But, cv mix = i xi ci = (0.4*0.742366) + (0.6*0.64957) = 0.6869 kJ/kg K
 Tmix = 367.46 K = 94.46oC
2 kg CO
120oC
3 bar
3 kg O2
75oC
5 bar

## Slide 14: Example 7.6 c
To get the partial pressures:
PCO = Pmix yCO = 3.82*0.432 = 1.651 bar
PO2 = Pmix yO2 = 3.82*0.568 = 2.171 bar
To get the entropy change:
Δs = Ʃ xi Δsi
Δs CO = cpCO ln Tmix/TA – RCO ln PCO/PA
= 1.039 ln (367.46 /393) – (8.314/28) ln (1.651 /3)
= 0.1075 kJ/kg K
Δs O2 = cPO2 ln Tmix/TB – RO2 ln PO2/PB
= 0.909 ln (367.46 /348) – (8.314/32) ln (2.171/5)
= 0.2663 kJ/kg K
ΔS = 0.4 * 0.1075 + 0.6 * 0.2663 = 0.20276 kJ/kg K
N.B.: Entropy increases because mixing is an irreversible process

## Slide 15: Example 7.7 a
Water is sprayed in an insulated de-superheater where it mixes with an entering superheated steam, to obtain saturated steam at the outlet. The conditions are: Inlet steam: ṁ= 0.3 kg/s , P= 27 bar, t=300 ºC; Inlet water: P= 29 bar, t=40 ºC; Outlet steam: P= 26 bar, saturated; Find the mass flow rate of water and outlet steam. Find also the entropy change of the system and the rate of entropy production assuming steady flow.
Answer:
System: Water (all phases) in the mixer (open steady flow)
Conservation: Mass and Energy
Energies: Enthalpies; No Work, No Heat.
Process: Mixing in a steady flow process
Properties: Inlet steam: Ps,in, Ts,in given  complete; Inlet water: Pw,in, Tw,in given  complete; Outlet steam: Ps,out given, saturated  given
Model: Steam tables
Extensive: Yes 1: mass of inlet steam
0.3 kg/s
27 bar
300oC
26 bar
Sat steam
29 bar
40oC

## Slide 16: Example 7.7 b
The mass balance gives
ṁs,out = ṁs,in + ṁw,in
so ṁs,out = 0.3 + ṁw,in (1)
The energy balance gives (neglecting KE and PE):
Q – W = Ʃ ṁi hi  ṁs,in hs in + ṁw,in hw,in = ṁs,out hs,out (2)
From steam tables at:
27 bar, 300 ºC  hs,in = 3004 kJ/kg, ss,in = 6.609 kJ/kg K
26 bar, saturated  hs,out = 2803 kJ/kg, ss,out = 6.24 kJ/kg K
Water 40 ºC  hw,in = 170 kJ/kg, sw,in = 0.572 kJ/kg K
Substituting in (2)
0.3*3004 + ṁw,in * 170 = (0.3 + ṁw,in)* 2803
Using (1)
ṁw,in = 0.023 kg/s
ṁs,out = 0.323 kg/s
the change in entropy for the system = 0 because it is in a steady state flow.
To get the rate of entropy production:
dS irrev / dt = Si ṁi si – Qr/Tr
= - ṁs,in ss,in - ṁw,in sw,in + ṁs,out ss,out
= - 0.3*6.609 – 0.023*0.572 + 0.323*6.242
= 0.0203 kW/K
N.B. Process is irreversible; hence dSirrev/dt must be positive
0.3 kg/s
27 bar
300oC
26 bar
Sat steam
29 bar
40oC

## Slide 17: Example 7.8 a
A vertical frictionless piston and cylinder arrangement has a cross-sectional area of 100 cm2 contains air initially at 27oC. Piston mass is 120kg, while atmospheric pressure is 1bar. Air is heated by an external heat reservoir having a temperature of 527oC, as a result cylinder height has increased from 20 to 40 cm. Assuming (a) ideal gas as well as (b) semi-ideal gas, find final temperature, as well as heat and work exchanged. Find also change of entropy of air, as well as entropy production of the universe due to this process.
Answer:
System: 4 systems: 1) Piston;
2) Air in the cylinder (closed);
3) Reservoir; 4) Universe
Conservation: Momentum in system 1;
Energy in system 2 and 3
Energies: Heat, Work and Internal energy
Process: Isobaric for system 2
Properties:
System 1: mass, area and atmospheric pressure  pressure in cylinder;
System 2) initial state: T1 and V1 given,
P1 from system 1  v1 and mair
final state: V2 given, P2 = P1  given ; System 3: Tres given
Model: a) Ideal and b) semi-ideal gas
Extensive: Yes 2: V1 and V2
100 cm2
1 bar
120 kg
Air
t1=27oC
20  40 cm
527oC

## Slide 18: Example 7.8 b
System 1: Piston
Absolute pressure is the sum of air pressure and piston weight:
P = 120*9.8/(100*10-4)/105 + 1 = 2.18 bar
System 2: Air in cylinder
V1 = 100*10-4 * 20*10-2 = 0.002 m3; V2 = V1 *4/2 = 0.004 m3
mair = PV1/RT1 = 2.18*105 * 0.002/ ((8314.5/28.9)*(273+27)) = 0.005052 kg
T2 = T1 * V2/V1 = 300 * 4/2 = 600 K (isobaric and ideal gas)
Work W = PdV = 2.18*105*(0.004 – 0.002) = 436 J
Heat Q: Qair = W + mair Du
    Ideal gas: Du = cv (T2 – T1) = 716.86 * (600 – 300) = 215,357 J/kg
Qair = W + mair Du = 436 + 0.005052 * 215,357 = 1,526 J
DSair = mair cP ln (T2/T1) = 3.5258 J/K
b) Semi-ideal gas: Du = u2 – u1 = 435.59 – 213.95 = 221.64 kJ/kg
Qair = 436 + 0.005052*221.64*1,000 = 1,555.63 J
DSair = mair (so(T2) – so(T1)) = 0.005052 *(2.4106 – 1.7015)*1,000 = 3.582 J/K
System 3: Reservoir
Qres = - Qair
DSres = Qres / Tres
    Ideal gas: DSres = – 1.9075 J/K
    Semi-ideal gas: DSres
    = – 1.9445 J/K
System 4: Universe
DSirrev = DSres + DSair
a) Ideal gas: DSirrev = 3.5258 – 1.9075 = 1.6183 J/K
b) Semi ideal gas: DSirrev = 3.582 – 1.9445 = 1.6375 J/K
(NB.: positive because irreversible)

## Slide 19: Example 7.9 a
Water enters a frictionless tube at 2 bar, 50oC and a rate of 0.5 kg/s. The tube is heated by an external heat reservoir at 290oC, until a dryness fraction (quality) of 0.9 is reached at exit. Find final temperature as well as mechanical power and rate of heat exchanged. Find the rate of entropy production.
Answer:
System: 1) Water (all phases) in the (open steady flow);
2) Reservoir; 3) Universe
Conservation: Energy
Energies: Heat and Enthalpy; No Work.
Process: Isobaric in a steady flow process
Properties: Inlet steam: Ps,in, Ts,in given  complete;
Outlet steam: isobaric & dryness fraction  given
Model: Steam tables
Extensive: Yes 1: mass flowrate of inlet steam
290oC
0.5 kg/s of H2O
50oC, 2 bar
xout=0.9

## Slide 20: Example 7.9 b
For isobaric flow in a frictionless tube:
Ẇ = 0
From first law for a steady flow process:
Q̇ = ṁ (h2 – h1) = 0.5 * (2486.4 – 209.5) = 1138.4 kW
System 1:
At inlet, temperature is lower than saturation
at the same pressure. Hence inlet fluid is in liquid state
Hence h1 = 209.5 kJ/kg; s1 = sf = 703.7 J/kgK
For exit conditions at P = 2bar, x2 = 0.9: wet steam.
T2 = Tsat = 120.23oC
hf = 504.68 kJ/kg ; hg = 2706.6 kJ/kg;
sf = 1.53 kJ/kgK; sg = 7.1271 kJ/kgK.
Hence:
h2 = (1-x2) hf + x2 hg = 2486.4 kJ/kg
s2 = (1-x2) sf + x2 sg = 6.5674 kJ/kgK
System 2: Reservoir
Ṡres = Q̇res / Tres = – 1138.4 / (290+273)
= – 2.022 kW/K
290oC
0.5 kg/s of H2O
50oC, 2 bar
xout=0.9

## Slide 21: Example 7.9 c
System 3 : Universe
Rate of entropy production:
Rate of entropy production is the total rate of entropy increase of the universe
It is composed of two components: change in Reservoir + change in Steam
Entropy change of the heat reservoir: – 2.022 kW/K
Entropy change of steam:
The latter is composed of two parts: steam inside tube and steam outside tube
  Steam inside the tube
Inside the tube: dS/dt = 0 because steady state
  Steam outside the tube
Outside the tube: 0.5 kg/s have changed their entropy from s1 to s2
Ṡsteam = ṁ (s2 – s1) = 0.5*(6.5674 - 703.7/1000) = 2.932 kW/K
 Total rate of entropy production is:
Ṡirrev = 2.932 – 2.022 = 0.91 kW/K